## Slide 1: Team <Team Name>
Case Study No. 3
<College>
<Member 1> · <Member 2> · <Member 3>
VeriQ: Experience-Verified, Intent-Aware QoS

## Slide 2
VeriQ: Experience-Verified, Intent-Aware QoS for the mixed-traffic home
Case Study 3 · MCV · Adaptive QoS Engine for Mixed Home Broadband Traffic | Team <Team Name> · <College>
The real problem
• Queues, not bandwidth: a backup upload filled the modem's oversized FIFO and added 266 ms (p95) to every packet in our Day-0 lab (emulated, 5 Mbit up)
• QUIC/TLS on port 443 defeats port rules; apps rarely set DSCP
• Capacity moves (DOCSIS, 5G FWA, Wi-Fi): a static shaper is bloated or wasteful
Our idea
“Other QoS engines guess. VeriQ verifies.”
Every policy change is a hypothesis: applied as a canary, tested on real experience metrics, kept only if it measurably helps, otherwise rolled back automatically, with an experience receipt.
Safety by design
• Never reads payload: headers + timing only; IPv4 + IPv6
• Every class keeps a non-zero floor: no starvation
• Abstains when unsure (conformal confidence)
• Versioned, reversible policies; watchdog → known-safe profile in < 1 s
Closed loop: observe → understand → decide → enforce → verify → commit or roll back
Observe
eBPF flow observer on tc clsact: sizes, timing, direction of first 30 packets; v4/v6; no payload
Understand
Early classifier with calibrated conformal confidence + capacity estimator (one-way-delay / STAMP probes, change-point)
Decide
Control loop on queuing delay · shaper = μ − kσ · intents with TTL · fairness floors
Enforce
CAKE / HTB via netlink: transactional apply, readback, rollback
Verify
Canary statistics on E-model MOS, WebRTC freezes, IETF RPM, Jain fairness
Show & control
Grafana · live 3D home-network twin · intent API (REST, TR-181 / USP)
What makes it different
1 Experience-verified policy transactions: canary → bootstrap CI / Mann-Whitney on p95 delay and MOS → commit or auto-rollback, each with a receipt
2 Real-app evidence: real encrypted WebRTC calls and DASH players in headless Chromium; we count video freezes and rebuffers, not just pings
3 Payload-free, calibrated classification: conformal sets → abstain when unsure; one-click correction feeds retraining; accuracy reported per privacy tier
4 Uncertainty-aware capacity tracking: Bayesian change-point + delay probes, up and down separately, link-layer overhead compensated
How we will prove it
• One-command netns lab, 5 arms: FIFO · fq_codel · static CAKE (SQM) · cake-autorate-style · VeriQ; ≥10 runs, 95% CIs, auto PDF report
• 8 scenarios: ISO during a call, 100 → 20 Mbps drop, 3 TVs + gaming, backup upload, chaos kill, IPv6…
• Live physical kit: Raspberry Pi 5 router + red “WAN DROP” button + chaos button
Targets: real-time added delay p95 ≤ 10 ms · settle < 2 s after WAN drop · zero starvation · CPU measured on ARM
Stack: Linux tc (CAKE · HTB · fq_codel; DualPI2/L4S-ready) · eBPF (libbpf CO-RE) · Python/Go control plane · LightGBM + conformal · Prometheus/Grafana · React + three.js · Flent / irtt / iperf3 / Playwright
Industry path: RDK-B / OpenWrt package · TR-181 data model + TR-369 USP for fleet control · EDT + eBPF + sch_fq for multi-gig PON · closed-loop home edge for intent-based network ops